## Slide 1: PulseSync: An Efficient and Scalable Clock Synchronization Protocol
2020.02.26
Christoph Lenzen, Philipp Sommer, and Roger Wattenhofer

## Slide 2: Problem
Challenges
• Accuracy
• Latency
• Efficiency
Problem：
  Existing protocols fail to achieve timely and accurate synchronization over larger distances.
  Most existing synchronization protocols cannot adapt quickly to changes in clock drifts or network connectivity.

## Slide 3: Contributions
Timely and accurate synchronization over large distances in multi hop networks
Adapt quickly to changes in clock drifts or network connectivity by flooding rapid, short “pulses” through the network.
Save energy : there is no need for nodes to listen between pulses once they detected any pulse, both on initialization or when joining the network later on.

## Slide 4: Model
a wireless network
the network as a static graph G = (V,E)
Focus on the following aspects:
Communication is expensive ： nodes send and receive one message per beacon interval B only.
Communication is inexact ： model them as independently distributed random variables and refer to the respective standard deviation as jitter J.
Sending times are constrained ： define the time it takes in each beacon interval between a node receiving and sending a message to be predefined and immutable by the algorithm.
Message size is constrained ： restrict the “payload” of a message to a small (constant) number of values.
Dynamics ： addressed by the proposed algorithm, which strives for dependency of computed clock values on a short period of time.

## Slide 5: Formalize the problem
Each node v ∈ V has a local hardware clock
The relative drift of is bounded (Typical hardware clocks exhibit drifts of at most 50 ppm)
A clock synchronization algorithm is asked to derive at each node v a logical clock based on local computations, its hardware clock readings, and the messages exchanged.
Goal :
  minimize the global skew G(t)
  using few messages and only recent information.
root node r ∈ V that has a perfect clock, i.e., at all times t .
nodes try to synchronize their logical clocks with .
minimizing the global skew is essentially equivalent to synchronizing clocks to

## Slide 6: PulseSync
The central idea : distribute information on clock values as fast as possible, while minimizing the number of messages required to do so.
  a node cannot forward any information it has not received yet
  node ought to forward the derived estimate as quickly as possible
  To keep the number of hops small : the flooding takes place on a breadth-first search (BFS) tree.
how nodes that are not children of the root obtain accurate estimates of r’s clock
  Simple Forwarding
  Drift Compensation

## Slide 7: Simple Forwarding
The time span = the time when it can send a (derived) estimate to its children - the time when node v receives a clock estimate from a parent
Simple Forwarding：
  at time t ，v obtains an estimate of the root’s clock value
  at time v sends the value to its children
the quality of the estimate :
is small ,negligible：

## Slide 8: Drift Compensation
use an independent estimate of to compensate the drift.
How to get ?
  given
  node v computes the regression line defining according to the k/2 most recent messages only.
  The remaining k/2 messages nodes may take information from are used to provide clock estimates with simple forwarding.
  The second regression line’s slope s should be close to
  ∈[1-ρ，1+ρ]，so 1/s∈[1-ρ，1+ρ]
How to compensate ?
at time , send
include into the message.

## Slide 9: Pseudocode

## Slide 10: IMPLEMENTATION
OS：TinyOS 2.x
Hardware Platform：the Opal wireless sensor network platform
The hardware clock is built on top of a 16-bit hardware clock register plus an additional 16-bit software counter
PulseSync Implementation：
  Initialization phase：
    setting the logical clock to the current hardware clock value
    nodes start overhearing the wireless channel for synchronization messages
  The bootstrap phase：
    If no synchronization messages have been received for a certain time, the node will declare itself as the reference node and starts to broadcast periodic synchronization pulses.
  Then:
    a node will receive periodic pulses from nodes located closer to the reference node

## Slide 11: EVALUATION
Compare ：Flooding Time synchronization Protocol（FTSP）
A. Testbed Setup
  an indoor testbed of 31 Opal nodes, which are placed in close proximity
  a network diameter of 30 hops
B. Measurement Results
  a four hour run
  roughly 44,600 data points were collected
  almost no packet loss

## Slide 12: EVALUATION
Initialization Phase

## Slide 13: EVALUATION
Synchronization Accuracy

## Slide 14: EVALUATION
Slow Forwarding of Clock Estimates
  nodes wait 300 milliseconds before forwarding the received clock estimates

## Slide 15
Thanks