## Slide 1: A High-Speed Load-Balancer Design with Guaranteed Per-Connection-Consistency
Tom Barbette, Chen Tang, Haoran Yao, Dejan Kostić, Gerald Q. Maguire Jr.,
Panagiotis Papadimitratos, and Marco Chiesa, KTH Royal Institute of Technology
nsdi'20
黄家晏
2020/10/30
Notes: 高速负载均衡器设计，保证每个连接的一致性

## Slide 2: Challenges
Large service providers use load balancers to dispatch millions of incoming connections per second towards thousands of servers.
Two basic yet critical requirements for a load balancer:
  uniform load distribution of the incoming connections across the servers
  per-connection-consistency (PCC)
The challenge: Ensuring PCC
  For each packet of an existing connection, the LB asks itself
  Which server is handling this connection?
  Today's solutions cannot ensure all requirements at the same times

## Slide 3: Background
Datacenter operators assign a Virtual IP (VIP) address to each operated service.
Each VIP in a DC is associated with a set of servers providing that service.
Each server has a Direct IP (DIP) address that uniquely identifies the server within the DC.
A LB inside the DC is a device that receives incoming connections for a certain VIP and selects a server to provide the requested service.

## Slide 4: CHEETAH
Which server is handling this connection?
  CHEETAH: ask the user to remember for us
  Key idea: store information about the load balancing decisions into a cookie
  Properties:
  dynamicity
  per-connection-consistency
  uniform load distribution
  efficient packet processing
  resilience

## Slide 5: Stateless CHEETAH LB
Encoding an opaque offset into the cookie.
an AllServers table that maps a server identifier to the DIP of the server
a VIPToServers table that maps each VIP to the set of servers running that VIP.
Stateless CHEETAH guarantees PCC.
Stateless CHEETAH supports arbitrary load balancing mechanisms.

## Slide 6: Stateful CHEETAH LB
support a finer level of visibility into the flows than that offered by stateless LBs.
A stateful LB can keep track of the behaviour of each individual connection and support complex network functions.
encoding table indices in the packet header.
store a set of m ConnTable tables that keep per-connection statistics and DIP mappings.
use an equal number of ConnStack stacks of indices, each storing the unused entries in its corresponding ConnTable.

## Slide 7: Evaluation
Packet Processing Analysis
Load Imbalance Analysis
PCC Violations Analysis

## Slide 8: Evaluation
Packet Processing Analysis
Stateless CHEETAH incurs minimal packet processing costs.
Stateful CHEETAH outperforms cuckoo-hash based LBs.

## Slide 9: Evaluation
Load Imbalance Analysis
CHEETAH reduces the 99th percentile FCT by a factor of 2 − 3x compared to the best performing hash-based mechanism, i.e., Hash RSS.

## Slide 10: Evaluation
PCC Violations Analysis
Cheetah not only achieves better load balancing with AWRR, but it also does not break any connection.

## Slide 11: Thanks